## Slide 1: Spatiotemporal modelling & automated in-situ sensors to monitor Harmful Algal Blooms(HABs) Case Study-Lake Victoria
Presenter:
Name: OKELLO, JACOB OKOMO
Reg. No: ENC222-0149/2017
Final Presentation

## Slide 2
HAB is a phenomena which turns water bodies dark blue-green due to eutrophication; potentially harming humans and animals e.g., massive fish deaths, etc.as lately observed in eutrophicated L. Victoria riparian. (Hecky et al., 2010)
Development, stability, and density of the phenomenon affect some environmental factors Lake Surface Air Temperature (LSAT), Sea Surface Temperature (SST) & Water surface spectral signatures (Tang et al, 2006)
The status quo only provides for the higher authority to solely rely on calls/information from the locals after the condition is a total mess without relying on any near real-time space-based or in-situ monitoring system.
Therefore, there’s need to come up with a quick response methodological approach to use space-based techniques and in-situ sensors to detect and alert the near-real time occurrence of HABs
Coupling wide spread spatiotemporal monitoring, and automated in-situ system will play a big deal in return. This would inform the Govt. and the general public the affected zones, calling for immediate remedy actions.
Introduction

## Slide 3: General and Specific objectives
To detect, monitor and report the occurrence of Harmful Algal Blooms(HABs) in Lake Victoria, Kisumu basin from 2015 to 2020 and beyond.
  To monitor chlorophyl-a (chl-a) concentration from L8 OLI.
  To monitor Lake Surface Air Temperature(LSAT) from L8 TIRS images as another HAB indicator in L. Victoria.
  To develop automated Internet of Things (IoT) in situ system, applicable in near real-time to monitor and report geo-tagged Water quality data.

## Slide 4: Study Area: Lake Victoria Nyanza Gulf
NYANZA GULF
Homabay

## Slide 5: Data and Materials
Tool/Material | Role | Availability
Google Earth Engine (GEE) | Geocomputation & Processing | Freely Available
ArcMap, R & Python | Further Analysis & Maps | 
Microcontroller & Sensors | In-Situ data Monitoring | Local Purchase
Data Type | Source | Role/Use
Landsat 8 OLI (30m, 16 days) | USGS (2015-2021) | Spatiotemporal HAB Monitoring
Landsat 8 TIR (100m, 16 days) | USGS (2015-2021) | Lake Surface Air Temperature (LSAT) Monitoring.
Field Data | Kenya Marine & Fisheries Research Institute-KMFRI (2015-2020) | Previous HAB events
In-Situ Data | In-situ System 2021 Onwards | Continued In-Situ Algal Monitoring

## Slide 6
B5 NIR
Lake Surface Emissivity (LSE)ε
At-Sensor Spectral Radiance to Brightness Temp (Tb10)
Estimate Lake Surface Air Temp (LSAT)
Automatic Results Download
Landsat 8 images
B3 GREEN
B2 BLUE
TIRS Data
OLI Data
B4 RED
NDVI
Automatic L8 Acquisition from GEE
TOA DN to At-Sensor Radiance(Lλ)
Validation
Above
Below
Ocean Color Chl-a algorithms
Process validation
Proportional of Vegetation(Pv)
TIRS B10
Threshold
Objective 1
Objective 2
Spatiotemporal Monitoring
Estimate for next available date
Estimate for next available date

## Slide 7: Overall methodology for IoT system
Start
LSAT
Salinity Status
In-situ data > Temp. threshold
GPS
Ensure a secure connection via SSh
IoT Gateway
No
Upload in-situ data to Local DB
Upload in-situ data to Reporter
Objective 3

## Slide 8: HAB reported dates, from 2015
Table 3: HABs reported in Lake Victoria, (KMFRI, NASA Earth Data)

## Slide 9: Results: Chl-a concentration maps
12th January 2015 23rd Feb 2016
04th September 2017 27th January 2018

## Slide 10: Accuracy Assessment of Chl-a Estimates
Year | Correlation Co-eff’
2015 | 0.836884
2016 | 0.883304
2017 | 0.891017
2018 | 0.843381
2019 | 0.899546
2020 | 0.900772
R = 0.836884

## Slide 11: Results (b): High LSAT recorded during bloom Events
12th January 2015 23rd February 2016
04th September 2017 27th January 2018

## Slide 12: Accuracy Assessment of LSAT Estimates
Year | Correlation Co-eff’
2015 | 0.698326
2016 | 0.71064
2017 | 0.691017
2018 | 0.713381
2019 | 0.71546
2020 | 0.70726
R = 0.698326

## Slide 13: Obtaining Information from Sensors: GPS Location, System Condition, Air Temperatures

## Slide 14: Discussions
The max. Chl-a values ranged from 31, 48, 57 and 50 Mg/ M3 which are significantly above the optimal (1 to 20Mg/ M3) in a non-turbid water body like Lake Victoria.
Corresponding LSAT Maps were generated for the reported HAB dates and reported to have risen to ~35˚C and ~36˚C in HAB events unlike aprox. ~25˚C for normal conditions.
The chl-a and LSAT estimates were validated with well known products and found to correlate from 69% to 90%.

## Slide 15: Conclusions and Recommendations
Wide spread chl-a concentration maps were generated from the proposed methodology to monitor HABs.
Corresponding LSAT maps were as well generated from the and reportedly, the LSAT rose on bloom events.
Chl-a and LSAT estimates were validated
Autonomous In-situ IoT system was developed and tested in local University water bodies and found capable of relaying near-real time geotagged data.
Recommendation
Authorities like KMFRI to avail detailed HAB stats, availability of Salinity sensor

## Slide 16: Thank you for your attention! Questions?